| 國立宜蘭大學一○二學年度第一學期期末考試試題紙 | 第 1 頁 |
| --- | --- |
| 考 試 科 目 | 班 級 | 學 號 | 姓 名 |
| 生物生產單元操作 | 生物機電四 |  |  |

Part I. Explanation (Please list its Chinese term and SI unit) (28%)

1.Ton of refrigeration:									2.Freeze Concentration:

3.EER:													4.Thermoelectric Cooling:

Part II. Problems (72%)

1. What is the mechanical vapor-compression refrigeration system? (24%)

2. What is the absorption refrigeration system? (12%)

3. Why IQF can keep the quality of the frozen food material? (12%)

4. Why the CFC products were banned by the Montreal Protocol on Substances that Deplete the Ozone Layer? (12%)

5. Calculate the cooling load (kcal/hr) present in a walk-in chamber, caused by the heat evolution of 10,000 kg of banana stored at 10℃. (12%)

Part III. Bonus (30%)

A cold storage room is being maintained at 2℃ using a vapor-compression refrigeration system that uses R-134a.  The evaporator and condenser temperatures are -20 and 40℃, respectively.  The refrigeration load is 10 tons.  Calculate the mass flow rate of refrigerant, the compressor power requirement, and the C.O.P..  Assume the unit operators under saturated conditions and the compressor efficiency is 90%.