國立宜蘭大學生物機電學系

一○一學年度第一學期生物生產單元操作第一次隨堂考試

年級： 生機四 		學號：						姓名：						10/31/2012

Part I. Explanation  (Please list its Chinese term and SI unit) (28%)

1. Viscosity:										2. Porosity:

3. Fluid Power:									4. NPSH:

Part II. Problems (72%)

1. Use the relationship between shear stress and shear rate to describe the difference between Newtonian and Non-Newtonian liquids.  Besides, use the Herschel-Bulkley Model to express the characteristics of  Newtonian and various Non-Newtonian liquids. (25%)

2. A batch of 18 kg of food product has a moisture content of 200% dry basis.  Calculate how much water must be removed from this product to reduce its moisture content to 5% wet basis. (17%)

3. A centrifugal pump is to be located 4 m above the water level in a tank.  The pump will operate at a rate of 0.02 m3/sec.  The manufacture suggests a pump with a NPSHR at this flow rate as 3 m.  All frictional losses may be neglected except a heat exchanger between the pipe inlet and the pump suction that has a loss coefficient Cf = 15.   The pipe diameter is 10 cm and the water temperature is 30℃.  Is this pump suitable for the given conditions?  If cavitation occurs, how can we do to resolve the problem? (30%)

Given: The vapor pressure is 4.246 kPa at 30℃.

Part III. Bonus (30%)

- What is the title of the textbook we used in class?  Who are the authors? (12%)

- Calculate the Reynolds number for 25℃water flow in a 1-in nominal diameter sanitary pipe at 0.5 kg/sec.  What are the flow characteristics? (18%)